## Slide 1: Informing River Management by Quantifying the Effects of Flow Conditions on Key Ecological Processes
Caitlin Conn1,2, Phillip Bumpers1,2, Amy Rosemond1, Kyle McKay3, Mary Freeman4, Todd Rasmussen5, John Schramski6, Seth Wenger1,2
1Odum School of Ecology 2River Basin Center 3US Army Corps of Engineers4 US Geological Survey 5Warnell School of Forestry and Natural Resources 6College of Engineering
Notes: Good morning. My name is Caitlin Conn and I am a PhD student with the Odum School of Ecology, studying under Seth Wenger and Amy Rosemond and positioned in the River Basin Center. Today I’m going to be talking about a project that is currently happening on the Middle Oconee River. With funding from the US Army Corps of Engineers, the Middle Oconee Flow Ecology project, is an active collaboration between researchers from the Corps of Engineers, the USGS, and a number of different UGA institutions – the Odum School of Ecology, the Warnell School of Forestry and Natural Resources, the College of Engineering, and the River Basin Center. This collaboration continues a long history of research that has occurred through UGA and government agencies specifically on the Middle Oconee.
I bring up the collaborative nature and research history for a couple of reasons. One, I think it is this type of collaboration (between government agencies, policy and science focused centers like the River Basin center and researchers) that allows science to better inform management & policy and management & policy to better inform science.

## Slide 2: Middle Oconee River, Ben Burton Park
Notes: And two, I want to recognize the great wealth of knowledge that this project is building off of. The Middle Oconee River, and specifically this location has been the subject of at least five dissertations, including a wealth of knowledge on benthic communities and the hydrology of the system that go back for the better part of a century.

## Slide 3: Research Objectives
To quantify the effects of flow variability on ecological processes
To predict the impacts of different management & climate scenarios
Productivity
Prior Flow Quantity and Quality of Producers 
Nutrient Uptake
Notes: Specifically, our research aims to quantify how changes in flow affects ecosystem processes. We have chosen to examine productivity and nutrient uptake. I am examining and going ot refer to primary productivity, though we are also collecting some information on secondary production. It is important to note that when I refer to productivity, we are referring to a rate and not biomass. This rate, which is usually mg of oxygen per liter of water over time gives us an understanding of activity of the plant, and not just the amount that is there.
We hypothesize that prior flow conditions, through direct presence or absence of shear stress or through indirect effects to temperature, bed material, light, etc. impacts the quantity and quality of producers existing within the stream. And then that these different amonts, qualitites, and associations of producers result in varying activity levels, seen in oxygen production and nutrient uptake.
This is the type of information managers a policymakers need to understand the effects of water supply infrastructure and policy. Understanding how flow impacts ecosystem processes, allows us predict the impact of different management scenarios or climate scenarios. The Middle Oconee is a great study site for this question because there are also a variety of common management issues. Development of pumped off-stream storage and small-scale hydropower, coupled with recurring droughts, have resulted in periodic extreme low flows and elevated daily and seasonal flow variability. This context raises questions about effects on river biota and water quality for local and downstream consumptive and recreational uses.

## Slide 4: Primary Producer Community
Macrophytes
  Podostemum ceratophyllum
Photo credit: Phillip Bumpers, Caitlin Conn
Benthic algae
Phytoplankton
Notes: Now when we are looking at southeastern streams we have three primary groups of producers contributing to productivity and nutrient uptake. We have macrophytes or aquatic plants. I have two here, but Podostemum appears to be the dominant macrophyte in this system. We also have benthic algae which is the algae growing on the bed material at the bottom of the stream channel. And then finally we have all the photosynthetic organisms floating around in the water column, the phytoplankton.

## Slide 5: Flow Variability
Photo credit: Jennifer Pahl
Photo credit: Phillip Bumpers
Notes: And what we want to determine is how these producers and their associated activities change with changing flow conditions. I have here a few pictures from the Middle Oconee at different stages. You can also see that these are different times of the year. The one on the left is a few years older and was taken during the summer, while the one on the right was taken just this past spring. The one on the left is well under 100 cfs, and the one on the right was taken at just under 500 cfs. And the MO is a sixth order stream, so this system has yearly peak flows of around 7,000 cfs.
We want to know what both of these events, and all the intermediate scenarios, do to these ecosystem processes. What happens with extended low flows? What happens with higher frequencies of high flow events? We know climate change is expected to increase the prevalence of extreme events like this, and we know that different management scenarios can greatly alter these events too.

## Slide 6: Study Components
Hydrologic Model
Whole Stream Data Logging
Monthly Biomass Sampling
Chamber studies
Notes: This brings us to the start of our study. We began our first field season this year and we have a number of different components. For the sake of time, I am not going to go into great detail about any of these, but if you would like more information about study specifics, please find me after the talk.
As Dr. McKay mentioned earlier, he has engineering students that have been developing a 2-D hydrologic model that we are using to get flow, velocity and discharge, for a given area within the stream.
We have loggers deployed at the site that are recording dissolved oxygen on the whole stream level, as well as loggers for light and conductivity.
We are conducting monthly biomass sampling. We go out along multiple transects that we have placed in different stream environments, across light and velocity gradients, and we collect all the producers on the bed material. We we will then use this monthly sampling informtaion, along with the flow data from the hydrologic model to create a model that predicts our processes of interest.
And finally, we are developing chamber studies to try and isolate some of these producer communities and get a more mechanistic understanding of how their productivity and nutrient uptake changes.

## Slide 7: First Field Season
Photo credit: Phillip Bumpers, Caitlin Conn
Notes: So we have just started getting our data input, so I don’t have any quantitive data to share at the moment, but I do want to highlight some of the changes we want to quantify. On the left, I have a picture from our first monthly sampling in June. I think you can make out the long stretches of filamentous algae? These were stretching for many tens of meters downstream. On the right, I have a photo from just after our September sampling. The water was significantly lower and had been for a while. But only after a number of July and August storms that washed out all the prior growth that had developed. These are the exact changes that we want to quantify. We want to know what flow conditions led to these different states and then how these states change processes. Does the algae result in more, less or equal nutrient uptake than just the macrophytes that were there in July?

## Slide 8: Acknowledgements
Thank you!
The many undergraduates, fellow graduate students, and staff who have helped me in the field already:
  Carter Coleman, Marisa ValeCruz, James Wood, Doug Leasure, John Skaggs, Dinah Carlton, Garrett Frandson
Notes: And with that, I would like to thank the many people who have helped me in the field, and of course my funding source, US Army Corps of Engineers. And thank you for you time!

## Slide 9: “The success of river protection and rehabilitation/restoration depends upon understanding and accurately modelling relationship between hydrological patterns, fluvial disturbance and ecological responses in rivers and floodplains” – Arthington et al. 2010
Notes: And if you have any questions, I would be more than happy to take them.